## Slide 1: Together for the New Style of IT
HP Enterprise Technology & Solutions Summit 2015
Dublin, Ireland June 15-19
#HPETSS

## Slide 2: Daily operations with iMC
How to make your admin life easier with iMC
Fabien GIRAUD / June 19, 2015

## Slide 3: Confidential Disclosure Agreement
The information contained in this presentation is proprietary to Hewlett-Packard Company and is offered in confidence, subject to the terms and conditions of a binding Confidential Disclosure Agreement (CDA)
HP requires customers and partners to have signed a CDA in order to view this training
The information contained in this training is HP confidential
This presentation is NOT to be used as a ‘leave behind’ for customers and information may only be shared verbally with HP-external customers under NDA
This presentation may be shared with HP Channel partners under NDA in hard-copy or electronic format for internal training purposes only
Do not remove any classification labels, warnings or disclaimers on any slide or modify this presentation to change the classification level.
Do not remove this slide from the presentation
HP does not warrant or represent that it will introduce any product to which the information relates
The information contained herein is subject to change without notice
HP makes no warranties regarding the accuracy of this information
The only warranties for HP products and services are set forth in the express warranty statements accompanying such products and services
Nothing herein should be construed as constituting an additional warranty
HP shall not be liable for technical or editorial errors or omissions contained herein
Strict adherence to the HP standards of business conduct regarding this classification level is critical.
HP Confidential - provided to HP employees and HP Partners for internal training purposes only
Notes: Some of the information in this session may be confidential. If you are not an HP employee, you must have a confidential disclosure agreement on file with HP to participate in the remainder of this session. Partners and contract trainers that have these agreements in place are welcome to attend.
  Next slide, please.

## Slide 4: Abstract
Session to make you understand why and how iMC helps your life
AIMS
Why do we need to be helped in Network Admin / Support
What are the solutions ?
Why iMC ?
Live examples

## Slide 5: Introduction
Why do we need some help ?
Typical situation:
Connection Point | Network Device | Interface
L2P21 | Level2-AccessSW-1 | gig 2/0/5
L2P22 | Level2-AccessSW-1 | gig 2/0/6
Level 2 Support
1: Find where he is connected
2: Verify the configuration
3: If we are lucky, correct the issue through CLI
4: Call back the hotline so that they can call back end user and verify everything works now
Notes: In this very simple example, this can take hours (even perhaps days if level 2 needs to connect on each switch to find where the user is connected)

## Slide 6: Introduction
Why do we need some help ?
Ideal situation 1:
Support Team
Fix
Network management tools
Open a case
Get the case
At the end, support team can close the ticket so that customer is automatically notified
Notes: This is a typical example when the issue is located on the end client part. So difficult to automatically detect in a monitoring tool (since this can’t manage all end client Ips)

## Slide 7: Introduction
Why do we need some help ?
Ideal situation 1:
Support Team
Detect
Fix
Situation is fixed before the end user notices the issue
Network management tools
Notes: This is a typical example of an issue located on the server side. Since the management tool manages also servers, it can automatically detects alarm on this.

## Slide 8: Introduction
Solutions
To be able to solve this, we need
A monitoring tool which will monitor network performance, get alarms on the devices … and show this in an understandable way to the team
A service desk tool in order to manage some process when anomalies appear on the network
A management tool in order to bea ble to quickly make some corrective changes on the network from a central point
Some reporting tools to be able to keep an history, to generate some SLA, send some service reports …

## Slide 9: Introduction
Why iMC
Just because with iMC we have all these tools in a single pane of glass !!!
Fault
Alarms
Syslog & Trap Mgr
Configuration
Intelligent Configuration Center
Compliance Center
VLAN & ACL Manager
Accounting
Network Assets
Performance
Performance
Mgmt
Virtual Network Mgmt
Security
Security Control Center
FCAPS
IMC Platform
Add-On Modules
Remote Site Manager
VAN ConnectManager
Service Health Manager
App Perform. Manager
Intelligent Analysis Reporter
User Behavior Analyzer
Service Oper
Mgmt
Network Traffic Analyzer
User Access Manager
Endpoint Admission Defense
Branch Intelli. Mgmt System
TACACS+ Authent Manager
IPSec VPN Mgr
MPLS VPN Mgr
Wireless Services Mgr
QoS Mgr
vMon
Extended API
VAN Resource Automate Manager
VAN SDN Manager
VAN Fabric Manager
UC Health
Manager

## Slide 10: Demoer Task : Prerequisite – Connect users
Open RDP connection on 10.10.134.11 and connect (wired connection) John user with iNode
Open RDP connection on 10.10.0.98 and connect John user to Wireless SSID HPN-User

## Slide 11: AGENDA
Scenario 1
  Detect
  Diagnose
  Fix
  Check
Scenario 2
  Detect
  Diagnose
  Fix
  Check
Scenario 3
  Detect
  Diagnose
  Fix
  Check
Notes: If time, show the event correlation (root cause)

## Slide 12: Demoer Task : disable connection port of John
Disable port GigabitEthernet 1/0/16 of 5500-1 device (10.10.150.65) using iMC

## Slide 13: Scenario 1: Simple connection issue
End user detect an issue
The end user John can’t access anything anymore on the network Open a case on iMC – SOM (http://10.10.105.21:8080/servicedesk/)
Notes: Username: john / Password : hpn

## Slide 14: Scenario 1: Simple Connection issue
Admin team diagnostic
The Network support team receives an email:
Notes: If needed, connect with network support user such as fgiraud / hpn or clinzell / hpn

## Slide 15: Scenario 1: Simple Connection issue
Admin team diagnostic
Apparently John can’t access the network !!! First let’s find him
We are lucky, John is an authenticated user (through iMC / UAM)  let’s find him in the access logs

## Slide 16: Scenario 1: Simple Connection issue
Admin team diagnostic
Access details show that John is connected on device 5500-1 (10.10.150.65) on port 16

## Slide 17: Scenario 1: Simple Connection issue
Admin team diagnostic
If we’re not lucky (not an authenticated user) we need to ask him his IP address and then we can find him

## Slide 18: Scenario 1: Simple Connection issue
Admin team diagnostic
Let’s find this device / port
Apparently there is an issue with this port GigabitEthernet 1/0/16 …
Let’s check (click on the alarm)

## Slide 19: Scenario 1: Simple Connection issue
Admin team diagnostic
Apparently, interface is down
iMC suggest to first check if the interface is disabled, then verify the cable …
So let’s click on the interface

## Slide 20: Scenario 1: Simple Connection issue
Admin team : Fix
YES … We got it. Admin status is DOWN.
So let’s make it up back

## Slide 21: Scenario 1: Simple Connection issue
Admin team : Fix
After few seconds, Admin Status and Operational Status show as UP  Issue fixed (apparently)

## Slide 22: Scenario 1: Simple Connection issue
Admin team : Check
Let’s make some test
    Find John in the online users to check he is connected
    Try to ping his IP address

## Slide 23: Scenario 1: Simple Connection issue
Admin team : Close the case
Fill in the solution in the case and ask John to close (if everything is ok)

## Slide 24: Scenario 1: Simple Connection issue
Admin team : Check (who did it ?)
Check in the iMC logs if you can see who shutdown the port

## Slide 25: AGENDA
Scenario 1
  Detect
  Diagnose
  Fix
  Check
Scenario 2
  Detect
  Diagnose
  Fix
  Check
Scenario 3
  Detect
  Diagnose
  Fix
  Check
Notes: If time, show the event correlation (root cause)

## Slide 26: Demoer Task : Remove vlan 25 on a link
On the Custom Topology « Grenoble – Eybens Dynamic » Remove from Current Vlan the link between WLC-1 and 10504-1

## Slide 27: Scenario 2: More complex connection issue
End user detects an issue
The end user John has access to the network but can’t access some URL. Principally he can’t access the Intranet Corporate WebSite: CleanBusiness
Notes: Username: john / Password : hpn

## Slide 28: Scenario 2 : More complex connection issue
Admin team diagnostic
The Network support team receives an email:
Notes: If needed, connect with network support user such as fgiraud / hpn or clinzell / hpn

## Slide 29: Scenario 2 : More complex connection issue
Admin team diagnostic : Client Side
Some interesting details in the ticket. First one: wireless client
 Let’s search it
Apparently he is still online and connected on AP : hp560-ap11-fr

## Slide 30: Scenario 2 : More complex connection issue
Admin team diagnostic – Client Side: Troubleshooting feature (1)
Let’s diagnose if it is a wireless issue using the « Search Troubleshooting » feature
We’ll check access to the web site and DNS

## Slide 31: Scenario 2 : More complex connection issue
Admin team diagnostic – Client Side: Troubleshooting feature (2)
We can see the path used to communicate to DNS server and Website and if there is some issue with the access user
No Alarm at this point

## Slide 32: Scenario 2 : More complex connection issue
Admin team diagnostic – Client Side: Troubleshooting feature (3)
By clicking on RF Ping, we can see if there are some issue between AP and client
Still NO ISSUE (wireless link quality excellent !!!)

## Slide 33: Scenario 2 : More complex connection issue
Admin team diagnostic – Client Side: Troubleshooting feature (4)
Clicking on NQA information will make some NQA test along the path
The issue is still not there
Average Delay
Positive Jitter
Negative Jitter
One of the devices does not support NQA

## Slide 34: Scenario 2 : More complex connection issue
Admin team diagnostic – Client Side: Troubleshooting feature (5)
Let’s finish with Spectrum Analysis to verify there is no interference
No interference  we need to search otherwhere

## Slide 35: Scenario 2 : More complex connection issue
Admin team diagnostic – Client Side: just for fun
Where is the user and what kind of device is he using ???

## Slide 36: Scenario 2 : More complex connection issue
Admin team diagnostic – Intranet Site Side
The other interesting point in the case: « principal issue = no access to CleanBusiness web site »
We monitor it in APM  check
Working fine

## Slide 37: Scenario 2 : More complex connection issue
Admin team diagnostic – DNS Side
Perhaps this is a DNS issue … Let’s check in APM
Also working fine

## Slide 38: Scenario 2 : More complex connection issue
Admin team diagnostic – Issue between Client and Intranet Site
Let’s check if there is some configuration issue between the client and the URL
Remember, the path found previously:
So let’s find it on a map (Demo Building custom topology)
No alarm on the links

## Slide 39: Scenario 2 : More complex connection issue
Admin team diagnostic – Issue between Client and Intranet Site
Let’s check VLAN (25) configuration in this path
WE FOUND IT : VLAN 25 is not allowed between 10504-1 and WLC-1

## Slide 40: Scenario 2 : More complex connection issue
Fix
Need to allow VLAN 25 on this link … So easy 

## Slide 41: Scenario 2 : More complex connection issue
Check
If we connect on the customer PC, we can see that now cleanbusiness is accessible … Well done. We can close the case
Notes: Connect to 10,10,0,98 and open http://cleanbusiness.hpn.local/ to check

## Slide 42: AGENDA
Scenario 1
  Detect
  Diagnose
  Fix
  Check
Scenario 2
  Detect
  Diagnose
  Fix
  Check
Scenario 3
  Detect
  Diagnose
  Fix
  Check
Notes: If time, show the event correlation (root cause)

## Slide 43: Demoer Task : Start Jperf (server)
RDP on server 10.10.105.22 (administrator user)
Start JPERF (shortlink on the desktop):
Open configuration file named « DemoDailyOpServer.jperf » (located in My Documents)
Start Iperf by clicking on the corresponding button:

## Slide 44: Demoer Task : Start CPUStress
RDP on server 10.10.105.22 (administrator user)
Start CPUSTRESS (shortlink on the desktop) 4 times:
In each CPUSTRESS windows activate the 4 threads (by selecting each one), and put activity level to « Maximum »
At the end, the CPU load on the server should be arround 100%

## Slide 45: Demoer Task : Start Jperf (server)
RDP on server 10.10.0.98 (administrator user)
Start JPERF (shortlink on the desktop):
Open configuration file named « DemoDailyOpServer.jperf » (located in My Documents)
Start Iperf by clicking on the corresponding button:

## Slide 46: Scenario 3: Proactive detection
Automatic detection: multiple ways
Admin Team receives an email with some alarm on link usage
In the NOC room, the Demo Building Network swap to yellow color
In the alarm browser of the admin team: some Link usage alarms !!!
Notes: Verify perf data + verify topology + …

## Slide 47: Scenario 3: Proactive Detection
Diagnose: alarm details
Open the alarm details: seems that some links are over used
Click on Performance data to view when this began
And also in live

## Slide 48: Scenario 3: Proactive Detection
Diagnose: Topology
We can also see something is hapenning on the topology (Demo Building)
And see real time monitoring

## Slide 49: Scenario 3: Proactive Detection
Diagnose: Topology
And also (NEW !) we can already check which kind of application is generating « strange » traffic

## Slide 50: Scenario 3: Proactive Detection
Diagnose: Who, what and Why ?
Let’s find know which kind of traffic it is … using NTA

## Slide 51: Scenario 3: Proactive Detection
Diagnose: Who, what and Why ?
Type of traffic:
DevilOne traffic is between these two !
And this is my server SRV13

## Slide 52: Scenario 3: Proactive Detection
Diagnose: Who, what and Why ?
Other talkers ?
The second top talker session is more « normal »

## Slide 53: Scenario 3: Proactive Detection
Fix: 1rst option  ACL
One way to fix should be to add an ACL directly from iMC (using the 2 ip address we detected before)
And to deploy it on the switch

## Slide 54: Scenario 3: Proactive Detection
Fix: 2nd option – Diagnose a little bit more
Another clever option should be to check if it is an authenticated user (so we can blaim him and disconnect )  UBA
Apparently, this is John who is the devil

## Slide 55: Scenario 3: Proactive Detection
Fix: 2nd option  Kick Out
Find John in the online users:
First we blacklist the user (since on many OS, wireless reconnects automatically)
And then we can kickout

## Slide 56: Scenario 3: Proactive Detection
Check
On the real-time monitoring we see the traffic going done / And on the client computer : disconnected …

## Slide 57: Note for demoer
Don’t forget to unblacklist john at the end of the demo

## Slide 58: Scenario 3: Proactive Detection
Check
When trying to access http://10.10.105.22/imc it seems still slow
By the way there was another interesting alarm in the alarm browser …
Seems that the server is overloaded … So let’s see more details

## Slide 59: Scenario 3: Proactive Detection
Diagnose: application monitoring
Alarm details check …
Many services should be impacted by this one … including the URL we tested !

## Slide 60: Scenario 3: Proactive Detection
Diagnose:

## Slide 61: Scenario 3: Proactive Detection
Diagnose:
Apparently CPUSTRES.EXE process is using all the CPU !
Need to kill it

## Slide 62: Scenario 3: Proactive Detection
Fix
Kill CPUSTRESS application

## Slide 63: Scenario 3: Proactive Detection
Check
APP monitoring is now ok
And URL accessible fine

## Slide 64: Scenario 3: Bonus Track
Compliance Report
Check compliancy of the device configurations
Customizable

## Slide 65: Scenario 3: Bonus Track
Network Inspection (SHM)
Check the health of the network (CPU, speed, OSPF routes number …)
Customizable
Report available: HTML, Word, PDF

## Slide 66: Scenario 3: Bonus Track
BSD – Business Service Dashboard (Available Q4FY15)
Overview of corporate services (combine network, applications, servers …)
Health & availability
Details (capacity planning, alarms, topology …)

## Slide 67: Scenario 3: Bonus Track
BSD – Business Service Dashboard (Available Q4FY15)

## Slide 68: Please give us your feedback!

## Slide 69: Thank you
Contact information